## Slide 1: Machine Learning Inspired Energy-Efficient Hybrid Precoding for MmWave Massive MIMO Systems
2017-5-23
Xinyu Gao1, Linglong Dai1, Ying Sun1, Shuangfeng Han2, and Chih-Lin I2
1Department of Electronic Engineering, Tsinghua University
2Green Communication Research Center, China Mobile Research Institute
Notes: Good morning everyone. My name is Xinyu Gao from Tsinghua University. The title of my presentation is machine learning inspired energy-efficient hybrid precoding for mmWave massive MIMO systems. As we know, hybrid precoding is a promising low RF complexity technique for future mmWave MIMO systems. However, the existing architectures still require an energy-intensive analog network such as phase shifter network. In this paper, we will design a new energy-efficient architecture, and propose a new hybrid precoding scheme for the new architecture.

## Slide 2: Contents
Technical background
1
Proposed solution
2
Simulation results
3
4
Conclusions
Notes: This talk consists of 4 parts. At first, we will introduce the technical background.

## Slide 3: Advantages of mmWave massive MIMO
Advantages
  High frequency (30-300 GHz): wider bandwidth (20 MHz → 2 GHz)
  Short wavelength: larger antenna array (1~8 → 256~1024)
  Serious path-loss and blockage: more suitable for small cells
mmWave
High frequency
Short wavelength
Serious path-loss
Wide bandwidth
Large antenna array
Small cell
1000x data rates increase!
Notes: As we can see from the figure, mmWave enjoys lots of advantages. For example, the spectrum at mmWave is less crowed and we can provide much larger bandwidth. Moreover, a large antenna array is easy to arrange in a compact form to achieve higher array and multiplexing gains. Finally, mmWave is also appropriate for small-cell as the serious path-loss and high directive beam can avoid multi-cell interferences. In conclusion, mmWave massive MIMO can combine the roadmaps of 5G in an unified form and achieve 1000 times capacity increase

## Slide 4: Bottleneck of mmWave massive MIMO
Challenges
  Traditional fully digital MIMO: one RF chain for one antenna
  Large antenna array → Enormous number of RF chains
  RF chain is energy-intensive at mmWave (300 mW/RF chain)
  High energy consumption is the bottleneck problem
  256 antennas at BS → 76.8 W (only RF chains)
  Micro-cell BS in 4G (baseband + RF + transmit): → less than 10 W
How to reduce the number of RF chains?
Notes: However, realizing mmWave massive MIMO in practice is not a trivial task. One key challenge is that each antenna in MIMO systems usually requires one dedicated RF chain. This results in unaffordable hardware cost and energy consumption in mmWave massive MIMO systems，since the number of antennas becomes huge and the energy consumption of RF chain is high. (For example, at 60 GHz, one RF chain will consume 250 mW. If we consider a mmWave massive MIMO base station (BS) with 256 antennas, only the RF chains will consume 64 Watts, which is much higher than the that of current 4G micro-cell BS). Therefore, how to reduce the number of required RF chains is an urging problem to solve.

## Slide 5
Hybrid analog and digital precoding
Basic idea[Ayach’14]
  Decompose the high-dimension fully digital precoder
  High-dimension analog beamformer (realized by analog circuit)
  Low-dimension digital precoder (requires RF chains)
  MmWave MIMO channel is low-rank
  Limited number of data streams can be transmitted
  Low-dimension digital precoder is enough for multiplexing gain
[Ayach’14] O. El Ayach, et al., “Spatially sparse precoding in millimeter wave MIMO systems,” IEEE Trans. Wireless Commun., Sep. 2014.
Notes: To overcome this problem, hybrid precoding has been proposed. As shown in the figure, the basic idea of hybrid precoding is to decompose the conventional high-dimension fully digital precoder into two parts. The first one is the high-dimension analog beamformer realized by analog circuit, while the second one is the low-dimension digital precoder requiring a small number of RF chains. Since the mmWave MIMO channel is usually low-rank, it can only transmit a limited number of data streams simultaneously. Therefore, a low-dimension digital precoder is enough to achieve the multiplexing gain.

## Slide 6
Classical hybrid precoding architecture
Phase shifter (PS)-based architecture [Rial,16]
  Full array gain → near-optimal sum-rate performance
  Large number ( ) of energy-intensive PSs ( )
[Rial’16] R. Méndez-Rial, et al., “Hybrid MIMO architectures for millimeter wave communications: Phase shifters or switches?” IEEE Access, Jan. 2016.
Switch (SW)-based architecture [Rial,16]
  No array gain → serious performance loss
  Small number ( ) of energy-efficient SWs ( )
Can we make a better trade-off between performance and energy consumption?
Notes: The figure shows two classical hybrid precoding architectures. The first one is phase shifter based architecture, where each RF chain is connected to all antennas via phase shifters. It can achieve the full array gain and near-optimal performance. However, it usually requires a large number of phase shifters. Since the energy consumption of phase shifter is also considerable, for example, 4-bit phase shifter consumes 40mW, the phase shifter based architecture is still energy-intensive. The other one is switch based architecture, where each RF chain is connected to only one antenna via switch. It is the simplest hybrid precoding architecture with quite low energy consumption. However, it cannot achieve array gain, leading to serious performance loss.
Based on the discussion above, one may ask a question. Can we make a better trade-off between performance and energy consumption?

## Slide 7: Contents
Technical background
1
Proposed solution
2
Simulation results
3
4
Conclusions
Notes: Of course, the answer is “Yes”.

## Slide 8: Switch and inverter (SI)-based architecture
Basic idea
  Each RF chain is connected to a sub array with antennas
  Each RF chain-sub array pair consists of one inverter and switches
  Energy consumption is considerably low
  switches and inverters
  Both switch and inverter are energy-efficient ( )
Array gain
How to design hybrid precoding scheme for new architecture?
Lemma 1. When and , the ratio between the array gain achieved by SI- based architecture and that achieved by PS-based architecture with sufficiently high-resolution phase shifters can be presented by
Notes: To achieve this goal, we propose a switch and inverter based architecture as shown in the figure. Assume N is the number of antennas and N_RF is the number of RF chains. Then, the key feature of the proposed architecture is that each RF chain is connected to a sub array with M antennas via one inverter and M switches. As we only need N switches and N_RF inverters in total, and both switch and inverter are energy-efficient, the energy consumption of the proposed architecture is considerably low. Moreover, as proved in the lemma, the array gain achieved by the proposed architecture is close to the optimal phase shifter based architecture. It can be expected that the proposed architecture can achieve a better trade-off.
The remaining problem is how to design hybrid precoding scheme for the new architecture.

## Slide 9
Optimization problem
System model
Constraints
  Total transmit power constraint:
  Hardware constraint on analog beamformer:
: Analog beamformer ( )
, : Digital precoder ( )
Problem formulation
Non-convex!
Notes: To do this, we first show the problem formulation in this slide. The system model can be presented like this, where F_RF is the analog beamformer and F_BB is the digital precoder. The optimization problem that maximizing sum-rate of K single-antenna users can be presented like this. For the proposed architecture, the analog beamformer should be block diagonal matrix, and its nonzero elements only belong to {-1,1}. This hardware constraint is nonconvex, which makes the optimization problem difficult to solve.

## Slide 10
Employ cross-entropy (CE) algorithm to search
  The complexity of searching all possible ’s is unaffordable
  → possible ’s
  Employ CE algorithm developed from machine learning to search
  Search the solution space in a more intelligent way
  Obtain the near-optimal solution with significantly reduced complexity
Inspiration
Decouple the joint design of and
  Given , the constraints become convex
  Conventional scheme can be used to obtain based on
  The number of possible ’s is finite
  We can try all possible ’s to maximize the sum-rate
Notes: To solve this problem, we first decouple the joint design of F_RF and F_BB. We observe that given F_RF, the constraints become convex, and F_BB can be obtained by classical schemes, such as zero forcing, based on the effective channel. Since the number of possible F_RF is finite, the optimization problem actually can be solved by trying all possible F_RF.
However, this scheme will involve unaffordable complexity for a reasonably large N in mmWave MIMO systems. This means that we need to search the solution space in a more intelligent way to reduce the complexity. To do this, in this paper we employ the cross-entropy algorithm developed from machine learning to search F_RF.

## Slide 11: Principle of CE algorithm
Key idea
  Randomly generate candidates according to a probability distribution
  Compute sum-rate (objective value) for each candidate
  Select best candidates as “elite” samples ( )
  Update the probability distribution by minimizing the CE
Disadvantage of conventional CE algorithm
  All elite samples are treated as the same
  The elite sample with higher object value is more important
  Adaptively weight the elites → better performance?
Cross entropy:
Minimization
Notes: This slide explains the principle of CE algorithm. As shown in the figure, after setting a probability distribution for the solution, CE algorithm starts by randomly generating S candidates, and computing the corresponding object value for each one. Then, it selects S_elite best candidates as elites, and finally uses them to update the probability distribution by minimizing the cross-entropy, which can be interpreted as the distance between two probability distributions. Repeating such procedure, we can generate the solution close to the optimal one in the end. However, in conventional CE algorithm, all elites are treated as the same. In fact, the elite with higher object value must be more important for the update. This motivates us to adaptively weight the elites and propose an adaptive CE algorithm to achieve better performance.

## Slide 12: Adaptive CE (ACE)-based hybrid precoding
Step 1
  Randomly generate analog beamformers based on
  Compute digital precoders based on
Step 2
  Calculate the achievable sum-rate
  Sort in an descend order:
  Select elites as
Initialization
  Collect nonzero elements of in a vector
  Set the iteration counter
  Set the initial distribution ( )
Notes: This slide summarizes our proposed ACE-based hybrid precoding scheme. After the initializing the probability distribution, we first generate S analog beamformers and digital precoders in step 1. If zero forcing is adopted, the digital precoder can be presented like this. Then, in step 2, we select S_elite analog beamformers with largest sum-rate as elites.

## Slide 13: ACE-based hybrid precoding scheme
Step 4
  Update according to elites and weights
  Equivalent problem of weighted CE minimization
  Compute first-order derivative of and set them to zero
Step 3
  Calculate weight for each elite
Step 5
  Repeat Steps 1 - 4 for iterations
  Output as analog beamformer and as digital precoder
PDF of
Notes: Then, in step 3, we compute the weight for each elite like this. Note that this is the key step different from the convectional CE algorithm. Finally, in step 4, we update the probability distribution based on elites and their weights like this. After I iterations, we can obtain the near-optimal analog beamformer and digital precoder.

## Slide 14: Complexity analysis
Step 2
  ZF precoder, SINR is simplified as with complexity
Step 1
  Compute with complexity
  Compute with complexity
Step 3
  Calculate weights with complexity
Step 4
  Update probability distribution with complexity
Total complexity
  After iterations, the complexity is
  Comparable with LS algorithm, as and do not need to be large
Notes: The complexity analysis shows that the overall complexity of the proposed ACE-based hybrid precoding is this. It is comparable with the classical low-complexity LS algorithm.

## Slide 15: Contents
Technical background
1
Proposed solution
2
Simulation results
3
4
Conclusions
Notes: Next, we will provide simulation results to verify the advantages of our scheme.

## Slide 16: Achievable sum-rate comparison
Simulation setup
  Multipath channel model
  UPA with
  Complex gain:
  AoA/AoD:
Observations
  ACE algorithm outperforms CE algorithm with negligible complexity increase
  Obvious improvement vs AS-based hybrid precoding (SW-based architecture)
  Satisfying vs two-stage hybrid precoding (PS-based architecture)
[Rial’15] R. Méndez-Rial, et al., “Channel estimation and hybrid combining for mmWave: Phase shifters or switches?” in Proc. ITA Workshops, Feb. 2015.
[Alkhateeb’15] A. Alkhateeb, et al., “Limited feedback hybrid precoding for multi-user millimeter wave systems,” IEEE Trans. Wireless Commun., Nov. 2015.
Notes: This figure shows the achievable sum-rate comparison, where the red line is the proposed ACE-based hybrid precoding with switch inverter based architecture. Firstly, we observe that the ACE algorithm outperforms the conventional CE algorithm, that is the purple line, with negligible complexity increase. Moreover, it is also obvious that our scheme can achieve the performance much better than the AS hybrid precoding with switch based architecture, that is the green line, and close to the two-stage hybrid precoding with phase shifter based architecture, that is the blue line.

## Slide 17: Convergence
Simulation setup
  Multipath channel model
  UPA with
  Complex gain:
  AoA/AoD:
  SNR = 10 dB,
Observations
  ACE-based hybrid precoding converges with a small (e.g., )
  A relative small number of candidates is enough (e.g., )
Limited improvement!
Notes: This figure shows the convergence of the proposed ACE based hybrid precoding scheme. We observe that our scheme can converge with a small number of iterations, and a relative small number of candidates S is enough to guarantee the performance. Recalling the complexity analysis, we know that the complexity of our scheme is acceptable.

## Slide 18: Energy efficiency (EE) comparison
Observations
  ACE-based hybrid precoding achieves the highest EE
  Two-stage hybrid precoding only performs well when is small (e.g., )
Energy efficiency
  Two-stage hybrid precoding:
  AS-based hybrid precoding
  ACE-based hybrid precoding
  Simulation parameters
[Rial’16] R. Méndez-Rial, et al., “Hybrid MIMO architectures for millimeter wave communications: Phase shifters or switches?” IEEE Access, Jan. 2016
[Rappaport’13] T. S. Rappaport, et al., “Millimeter wave mobile communications for 5G cellular: It will work!” IEEE Access, May 2013
Notes: This figure shows that energy efficiency. The energy consumption model and adopted values are listed here. The red line is the energy efficiency of the proposed ACE-based hybrid precoding. We observe that our scheme can achieve the highest energy efficiency. By contrast, the two-stage hybrid precoding, that is the blue line, can only performs better than the fully digital precoding, that is the black line, when K is small.

## Slide 19: Contents
Technical background
1
Proposed solution
2
Simulation results
3
4
Conclusions
Notes: Finally, we will make a brief summary of this paper.

## Slide 20: Summary and conclusions
SI-based hybrid precoding architecture
  Design a new architecture with a small number of switches and inverters
  Enjoy low energy consumption and near-optimal array gain
ACE-based hybrid precoding scheme
  Propose an ACE algorithm with low complexity for the new architecture
  Achieve satisfying sum-rate performance and much higher EE
Notes: In this paper, we first propose a switch inverter based hybrid precoding architecture, where the analog part is realized by a small number of switches and inverters. It enjoys low energy consumption and near-optimal array gain. Then, by employing the idea of CE optimization in machine learning, we propose an ACE-based hybrid precoding scheme with low complexity for the new architecture. Simulation results verify that our scheme
can achieve the satisfying sum-rate performance and much higher energy efficiency than traditional schemes.

## Slide 21
Thank you !
Contact information
  Xinyu Gao
  xy-gao14@mails.tsinghua .edu.cn & xgao237@wisc.edu
Notes: That is all. Thanks for your attention.