## Slide 1: Near-Optimal Hybrid Analog and Digital Precoding for Downlink mmWave Massive MIMO Systems
Linglong Dai1, Xinyu Gao1, Jinguo Quan2, and Shuangfeng Han3, and Chih-Lin I3
2015-06-08
1Department of Electronic Engineering, Tsinghua University
2Division of Information Science & Technology, Tsinghua University
3Green Communication Research Center, China Mobile Research Institute
Notes: Good morning everyone! My name is Xinyu Gao, from Tsinghua University. The title of my presentation is Near-Optimal Hybrid Analog and Digital Precoding for Downlink mmWave Massive MIMO Systems.

## Slide 2: Contents
Technical Background
1
Proposed Solution
2
Complexity Analysis
3
Simulation Results
4
Conclusions
5
Notes: This presentation will consist of 5 parts, that is the technical background, proposed solution, complexity analysis, simulation results, and conclusion. At the beginning, let’s have a view of the technical background

## Slide 3: MmWave massive MIMO
Why mmWave?
Why mmWave + massive MIMO?
  Short wavelength enables large antenna array in massive MIMO
  Massive MIMO provides sufficient gains to compensate the serious path-loss by employing precoding
mmWave
High frequencies
Short wavelength
Serious path-loss
Spectrum expansion
Large antenna array
Small cell
1000x capacity increase!
Notes: As we can see from the figure, there are three special properties of mmWave. The first property is the high frequencies around and above 30GHz where the spectrum is less crowed. The second property is the short wavelength, enabling a large antenna array to be arranged in a compact form. The last property is the serious path-loss, making the smaller cell size more attractive for the mmWave communication. As a result, mmWave can combine the roadmap of 5G in an unified form, and therefore 1000 times capacity increase can be achieved.
Besides, since usually a large antenna array is employed by mmWave systems, it can provide sufficient gains to compensate the serious signal attenuation by using the precoding technique.

## Slide 4: Precoding for mmWave massive MIMO
Traditional precoding
  Preformed in digital domain
  One RF chain support one transmit antenna
  Impractical in hardware for the large antenna array
Hybrid precoding
  Two steps:
  Digital precoding with small size
  Analog precoding with large size (realized by phase shifter, PS)
  One RF chain support several transmit antennas
  Low hardware complexity without obvious performance loss
Notes: The traditional precoding is entirely realized in the digital domain to cancel the interferences between different data streams. Digital precoding requires an expensive radio frequency (RF) chain for every antenna. In mmWave massive MIMO with a large number of antennas, it will bring prohibitively high energy consumption and hardware complexity. To solve this problem, mmWave massive MIMO prefers the more energy-efficient hybrid precoding, which can significantly reduce the number of required RF chains. Specifically, the transmitted signals are first precoded by the digital precoding of a small size to guarantee the performance, and then precoded again by the analog precoding of a large size to save the energy consumption and reduce the hardware complexity.

## Slide 5: Existing hybrid precoding techniques
Two architectures of hybrid precoding
  Fully-connected
  Large number of PSs
  Near-optimal but energy-intensive
  Sub-connected
  Smaller number of PSs
  More energy-efficient
Fully-connected
  Spatially sparse precoding [Ayach’14]
  Codebook-based hybrid precoding [Roh’14]
Sub-connected
  Still a challenging problem
[1] O. El Ayach, et al., “Spatially sparse precoding in millimeter wave MIMO systems,” IEEE Trans. Wireless Commun., 2014.
[2] W. Roh, et al., “Millimeter-wave beamforming as an enabling technology for 5G cellular communications: Theoretical feasibility and prototype results,” IEEE Commun. Mag., 2014.
Notes: There are two architectures of hybrid precoding, the first one is the fully-connected architecture, where each RF chain is connected to all BS antennas via phase shifters. This architecture can achieve near-optimal performance. However, it still has two limitation. Firstly, it requires thousands of phase
shifters to realize the analog precoding, leading to both high energy consumption and hardware complexity. Second, each RF chain will drive hundreds of BS antennas, which is also energy-intensive. The second architecture is sub-connected one, where each RF chain is connected to only a subset of BS antennas. This architecture can reduce the number of required phase shifters without obvious performance loss, and therefore, more energy-efficient and practical for mmWave MIMO systems.
For the fully-connected architecture, there are already some excellent algorithms proposed recently, such as the spatially sparse precoding and the codebook-based hybrid precoding. However, the design of hybrid precoding with sub-connected architecture is still an open problem.

## Slide 6: Contents
Technical Background
1
Proposed Solution
2
Complexity Analysis
3
Simulation Results
4
Conclusions
5
Notes: In this paper, we will focus on sub-connected architecture and propose near-optimal hybrid analog and digital precoding.

## Slide 7: Problem formulation
System model
Total achievable rate
Three constraints
  Structure constraint:
  Amplitude constraint: All elements of have fixed amplitude
  Power constraint:
Target
  Jointly design A and D to maximize achievable rate
Notes:   At first, we need to formulate the problem. Consider the narrowband system, then, the received signals y can be presented by the first equation, where rho is the transmitted power, H is the channel matrix, A,D, and P are the analog, digital, and hybrid precoding matrices, respectively, s is the transmit signals with normalized power, and finally n is the noise. The corresponding total achievable rate R can be presented by the second equation. Our goal is jointly design A and D to maximize the achievable rate. Note that, here we have three constraint conditions, that is the structure constraint, amplitude constraint, and power constraint as listed here.

## Slide 8: SIC-based hybrid precoding
where is the nth column of P, , and
Decompose the total achievable rate
SIC-based hybrid precoding
  Total rate sub-rate of sub-antenna array
  Optimize the rate of each sub-antenna array one by one
Notes: To solve the total achievable rate optimization problem with non-convex constraints. In this paper, we propose to decompose the total achievable rate into the form in the blue color. From this equation, we can observe that total rate equals to the summation of each sub-rate of sub-antenna array. This inspires us to propose a successive interference cancelation (SIC)-based hybrid precoding, also called as SIC-based hybrid precoding. As shown in this figure, the basic idea of our method is to optimize the achievable sub-rate of the first sub-antenna array and update the matrix T1. Then, the similar method can be used to optimize the sub-rate of the second sub-antenna array. Such procedure will be executed until the last sub-antenna array is considered.

## Slide 9: Solution to the sub-rate optimization problem
Equivalent problem
  Consider non-zero elements
  Simplify the optimization problem
  Find sufficiently close to maximize the achievable sub-rate
Target
  Optimize achievable rate of the nth sub-antenna array
where
where ,
where is the first right singular vector of
Notes: Next, we will find the solution to the sub-rate optimization problem. Consider the nth sub-antenna array, the corresponding optimization problem can be presented by the first formula. Then, with some mathematical derivation, we know that this optimization problem is equivalent to the formula in the blue color. This indicates that maximizing the achievable sub-rate of each sub-antenna array is equivalent to simply seeking a precoding vector close to the vector v1.

## Slide 10: Design of analog and digital precoder
Problem
  Find to minimize
Solution
  Analog precoder:
  Digital precoder:
  Hybrid precoder:
  Easy to check all the three constraint conditions are satisfied
Summary of our method
  SVD of to obtain
  Compute for the nth sub-antenna array
  Update for the (n+1)th sub-antenna array
Notes: Based on the equation that pn equals dn multiply an, we can obtain the optimal analog, digital, and hybrid precoder as listed in this slide. It’s also easy to verify that our solution satisfies the three constraint conditions mentioned above. To sum up, our method can be described by three steps.
Step 1: Execute the SVD of matrix G_hat to obtain the first right singular vector v1;
Step 2: Compute the optimal solution to the current nth sub-antenna array;
Step 3: Update matrix G_hat for the next sub-antenna array.

## Slide 11: Contents
Technical Background
1
Proposed Solution
2
Complexity Analysis
3
Simulation Results
4
Conclusions
5
Notes: Next we will discuss the computational complexity of the proposed scheme.

## Slide 12: Complexity analysis
Computation of
  Only the first right singular vector of is required
  Realized by power iteration algorithm with complexity
Acquire the optimal precoder
  The complexity is only to obtain
Update
  The calculation can be simplified as
  Corresponding complexity is
Total complexity
  N RF chains
is largest singular value of
Notes:   Based on the description above, we know that the computational complexity of our method comes from three part. The first one is the computation of vector v1. Since only the first right singular vector of G_hat is required. This part can be realized by the standard methods such as power iteration algorithm . It’s complexity is in the order of M square. The second one comes from the computation of the optimal solution, this part is only in order of M. The last one is from the update of matrix G_hat. With some mathematical derivation, the updated G_hat can be approximated by the red formula. Therefore, this part involves the complexity in order of M square, too. To sum up, since there are N RF chains, the total complexity of our method is in order of N multiply M square.

## Slide 13: Contents
Technical Background
1
Proposed Solution
2
Complexity Analysis
3
Simulation Results
4
Conclusions
5
Notes: Next, we will show the simulation results to verify the near-optimal performance of our method.

## Slide 14: Simulation results
Simulation setup
  Antennas: (1) (2)
  RF chains: (1) (2)
  Channel: Geometric Saleh-Valenzuela model
SIC-based hybrid precoding is near-optimal！
Notes: The figure on the left side shows the achievable rate comparison, where the antenna configuration is 64 multiply 16 and the number of RF chains is 8. This blue line is the performance of our method. We can observe from this figure that the proposed SIC-based hybrid precoding outperforms the conventional analog precoding, that is the purple line. This figure also verifies the near-optimal performance of SIC-based hybrid precoding, since it can achieve about 99% of the rate achieved by the optimal and unconstrained precoding, that is the green line.
The figure on the right side compares the achievable rate where the antenna configuration is 128 multiply 32 and the number of RF chains is 16, where we can observe similar trends as those from the figure on the left side. More importantly, these two figures show that the performance of SIC based hybrid precoding is also close to the spatially sparse precoding and the optimal unconstrained precoding with fully-connected architecture, that is the red line and the black line, respectively. Considering the low energy consumption and computational complexity of the proposed SIC-based hybrid precoding, we can further conclude that SIC-based hybrid precoding can achieve much better trade-off among the performance, energy consumption, and computational complexity.

## Slide 15: Contents
Technical Background
1
Proposed Solution
2
Complexity Analysis
3
Simulation Results
4
Conclusions
5
Notes: In the end, we summarize this presentation and draw the conclusions.

## Slide 16: Conclusions
We proposed a SIC-based hybrid precoding with sub-connected architecture
Basic ideas:
1) Decompose the total achievable rate into sub-rate
2) Optimize the sub-rate of each sub-antenna array one by one
The computational complexity of our method is only
Simulation results verified the near-optimal performance of our method
Notes: In this paper, we proposed a SIC-based hybrid precoding with sub-connected architecture. The basic idea of our method is to decompose the total achievable rate into sub-rate, and then optimize the sub-rate of each sub-antenna array one by one.
Complexity evaluation showed that the complexity of our method is only in order of N multiply M square.
Simulation results verified the near-optimal performance of our method, and showed that the performance loss induced by sub-connected architecture is not obvious compared to the fully-connected architecture .

## Slide 17
Thanks for your attention !
Notes: That’s all. Thanks for your attention!