## Slide 1
Pattern-Division Multiplexing for
Continuous-Aperture MIMO
Zijian Zhang and Linglong Dai
16th May 2022
IEEE ICC 2022
Notes: Nice to meet you every one! I am Zijian Zhang from Tsinghua University. Today I wish to introduce our recent work titled “Pattern-Division Multiplexing for Continuous-Aperture MIMO”.

## Slide 2
  continuous-aperture MIMO (CAP-MIMO)
  Holographic MIMO, large intelligent surface
  The current density (pattern) is generated on the aperture of CAP-MIMO transmitter and the information-carrying electromagnetic wave is induced at the receiver
Continuous-aperture MIMO (CAP-MIMO)
A. Pizzo, T. L. Marzetta and L. Sanguinetti, "Spatially-stationary model for holographic MIMO small-scale fading," IEEE J. Sel. Areas Commun., vol. 38, no. 9, pp. 1964-1979, Sep. 2020.
Notes: At first, I would like to introduce the concept of CAP-MIMO. Continuous aperture MIMO, namely cap-mimo, also known as holographic MIMO or active intelligent hypersurface, is considered to be a typical example of the application of electromagnetic information theory. The earliest holographic MIMO concept was proposed by Professor marzetta in New York University to maximize the ultimate performance of wireless communications. An ideal cap-mimo can be considered as a fully adjustable quasi continuous electromagnetic surface, which can fully reconstruct the current density distribution on its surface to induce the information-carrying electromagnetic field in space, so as to actively send and receive the spatial electromagnetic waves.
科学问题3：带宽巨大的赫兹大规模天线系统将面临严重的波束分裂问题。在窄带情况下，波束赋形及天线间距按都是按信号的中心频点𝑓_𝑐来设计，比如天线间相位差由物理角度𝜃_0、天线间距d和中心频率的波长𝜆𝑐决定，其中天线间距d通常为半个波长，设计好就固定不动了。 我们来看在宽带信号情况下会有什么变化。 通过分析我们发现，如图所示，宽带情况下波束方向𝜃将随着信号的频率f变化而变化，频率变化范围越大，即信号带宽越大，波束方向变化也越大。我们期望天线阵列向某一个用户发射定向波束，但信号带宽过大，但有些子载波上的波束方向偏离了用户，即波束发生了分裂。这类似于带宽很大的白光通过三棱镜时发生的色散现象。 我们举个例子来说。对于2GHz带宽的毫米波信号而言，其波束较宽，不同频率导致的波束偏移为1.5度，相当于偏了13%，波束扩散不算太严重。但是，对于20GHz带宽的太赫兹信号而言，其波束宽度仅为3度，而波束偏移高达9度，相当于偏了300%！偏移量大大超过了波束宽度。由此可见，由于太赫兹信号的带宽很大，量变引起质变，毫米波里的波束偏移问题演变为太赫兹的波束分裂问题。

## Slide 3
  Channel modeling：Modeling small-scale fading of electromagnetic channel with Gaussian random field in wavenumber domain[1]
  DoF analysis: degrees of freedom of communication between two CAP-MIMO is analyzed[2]
  Transmission method: wavenumber-division multiplexing is proposed to modulate symbols on different wavenumbers[3]
CAP-MIMO: Prior works
[1] A. Pizzo, T. L. Marzetta and L. Sanguinetti, "Spatially-stationary model for holographic MIMO small-scale fading," IEEE J. Sel. Areas in Commun., vol. 38, no. 9, pp. 1964-1979, Sep. 2020.
[2] D. Dardari, "Communicating with large intelligent surfaces: Fundamental limits and models," IEEE J. Sel. Areas Commun., vol. 38, no. 11, pp. 2526-2537, Nov. 2020.
[3] L. Sanguinetti, A. D’Amico, M. Debbah, "Wavenumber-division multiplexing in line-of-sight holographic MIMO communications," arxiv preprint arxiv:2106.12531., Jun. 2021.
[1]
[2]
[3]
Notes: There are many hot topics of CAP-MIMO in the existing works. For example, in the first reference, the authors proposed to model the small-scale fading of electromagnetic channel with Gaussian random field in wavenumber domain. Then, in the second reference, the authors have analyzed the degrees of freedoms between a couple of CAP-MIMO, and many insightful results are obtained and many interesting phenomenons are revealed. Recently, in the third reference, the authors proposed a wavenumber-division multiplexing method to modulate different symbols on different wavenumbers. In this way, a multi-stream transmission like OFDM can be realized.
科学问题3：带宽巨大的赫兹大规模天线系统将面临严重的波束分裂问题。在窄带情况下，波束赋形及天线间距按都是按信号的中心频点𝑓_𝑐来设计，比如天线间相位差由物理角度𝜃_0、天线间距d和中心频率的波长𝜆𝑐决定，其中天线间距d通常为半个波长，设计好就固定不动了。 我们来看在宽带信号情况下会有什么变化。 通过分析我们发现，如图所示，宽带情况下波束方向𝜃将随着信号的频率f变化而变化，频率变化范围越大，即信号带宽越大，波束方向变化也越大。我们期望天线阵列向某一个用户发射定向波束，但信号带宽过大，但有些子载波上的波束方向偏离了用户，即波束发生了分裂。这类似于带宽很大的白光通过三棱镜时发生的色散现象。 我们举个例子来说。对于2GHz带宽的毫米波信号而言，其波束较宽，不同频率导致的波束偏移为1.5度，相当于偏了13%，波束扩散不算太严重。但是，对于20GHz带宽的太赫兹信号而言，其波束宽度仅为3度，而波束偏移高达9度，相当于偏了300%！偏移量大大超过了波束宽度。由此可见，由于太赫兹信号的带宽很大，量变引起质变，毫米波里的波束偏移问题演变为太赫兹的波束分裂问题。

## Slide 4
  Pattern-division multiplexing: modulate symbols on multiple patterns, and realize multi-stream transmission by designing continuous pattern functions
CAP-MIMO: Pattern-division multiplexing (PDM)
Combiner K
…
Combiner 1
Combiner 2
Users
CAP-MIMO Transmitter
Pattern for user 1
Pattern Design
…
…
Pattern for user 2
Pattern for user K
Electric field
Electric field
Notes: Specifically, the architecture of cap-mimo is shown above. Here, we show that a cap-mimo transmitter transmits electromagnetic signals works as a base station and several electromagnetic-wave receivers receive signals work as the users. Among them, the current density on the continuous aperture of cap-mimo can be divided into several current patterns, and different patterns are used to modulate different symbols for different users. Thus, by designing several pattern functions as orthogonal as possible, the spatial electric field induced by cap-mimo can serve several users with better performance. In this case, How to design continuous pattern functions for different users becomes our research problem.
科学问题3：带宽巨大的赫兹大规模天线系统将面临严重的波束分裂问题。在窄带情况下，波束赋形及天线间距按都是按信号的中心频点𝑓_𝑐来设计，比如天线间相位差由物理角度𝜃_0、天线间距d和中心频率的波长𝜆𝑐决定，其中天线间距d通常为半个波长，设计好就固定不动了。 我们来看在宽带信号情况下会有什么变化。 通过分析我们发现，如图所示，宽带情况下波束方向𝜃将随着信号的频率f变化而变化，频率变化范围越大，即信号带宽越大，波束方向变化也越大。我们期望天线阵列向某一个用户发射定向波束，但信号带宽过大，但有些子载波上的波束方向偏离了用户，即波束发生了分裂。这类似于带宽很大的白光通过三棱镜时发生的色散现象。 我们举个例子来说。对于2GHz带宽的毫米波信号而言，其波束较宽，不同频率导致的波束偏移为1.5度，相当于偏了13%，波束扩散不算太严重。但是，对于20GHz带宽的太赫兹信号而言，其波束宽度仅为3度，而波束偏移高达9度，相当于偏了300%！偏移量大大超过了波束宽度。由此可见，由于太赫兹信号的带宽很大，量变引起质变，毫米波里的波束偏移问题演变为太赫兹的波束分裂问题。

## Slide 5
  PDM：Sum-rate and power constraint
PDM: System model
Achievable rate for user k：
BS transmit power：
Sum-rate
Power constraint
Patter function
（current density）
Challenge：The optimization of continuous pattern functions
Z. Zhang and L. Dai, “Pattern-division multiplexing for continuous-aperture MIMO,” in Proc. 2022 IEEE International Conference on Communications (IEEE ICC’22), Seoul, South Korea, May 2020.
  PDM：Problem formulation
Notes: In order to design the current density of cap-mimo surface, we first need to model the optimization problem. Using the mutual information formula, we can calculate the achievable rate of user K. Along with the base station transmit power constraint, we can model the multi-user sum-rate maximization problem shown above. Where Pmax is the maximum available transmit power of the base station and thetak is the current density to be optimized. By solving this problem, we can get the pattern design and the maximum users’ sum-rate. However, the difficulty in solving this problem is the optimization of nonconvex functional pragramming. Specifically, different from the traditional precoding optimization for massive MIMO, cap-mimo, as a continuous electromagnetic surface, needs to design a series of continuous pattern functions thetak, which is difficult for the existing digital signal processing methods. Therefore, the existing methods often use some special functions with good mathmatical properties to realize the heuristic design thetak.

## Slide 6
  Design pattern functions based on orthogonal basis functions
PDM：Pattern design
Orthogonal basis projection of patterns：
Electric field：
Orthogonal basis functions：
Power constraint：
Z. Zhang and L. Dai, “Pattern-division multiplexing for continuous-aperture MIMO,” in Proc. 2022 IEEE International Conference on Communications (IEEE ICC’22), Seoul, South Korea, May 2020.
A general pattern design method for CAP-MIMO
  The design of pattern functions is transformed to that of projection lengths
Notes: Thus, in order to solve this problem, we propose a transform method based on Fourier transform, which transforms continuous function optimization into continuous variable optimization. By introducing the Fourier basis function psi, we can expand the pattern function and project the continuous functions into the Fourier space, so that the design of the continuous function is transformed into the projection length design in the Fourier basis space. Thus, we realize the discretization of electromagnetic waves and transmit power constraint. Since then, the continuous function design is transformed into discrete vector design, and the traditional digital signal processing method can be used to optimize the precoding problem again. In this way, we actually realize a general pattern design method for CAP-MIMO.

## Slide 7
  Simulation scenario
    1 CAP-MIMO Transmitter
    4 users
PDM: Simulation results
L. Sanguinetti, A. D’Amico, M. Debbah, "Wavenumber-division multiplexing in line-of-sight holographic MIMO communications," arxiv preprint arxiv:2106.12531., Jun. 2021.
Z. Zhang and L. Dai, “Pattern-division multiplexing for continuous-aperture MIMO,” in Proc. 2022 IEEE International Conference on Communications (IEEE ICC’22), Seoul, South Korea, May 2020.
  200%
Pattern amplitude
Pattern phase
Sum-rate vs. CAP-MIMO area
Notes: The last is our simulation results. On the left is the simulation scenario, including one cap-mimo and four electromagnetic receiving users. From the simulation results, we note that, compared with the traditional heuristic design based on special functions, the proposed continuous function design which is based on the basis expansion can nearly double the capacity compared with the "wavenumber-division multiplexing" design method in the existing literature, which is based on special functions. The patterns designed by the proposed scheme for different users are nearly orthogonal, which shows that the electromagnetic waves can reach multiple users as orthogonally as possible, and the beamforming enhancement is realized.

## Slide 8
Reproducible research：http://oa.ee.tsinghua.edu.cn/dailinglong/
IEEE ICC 2022
Notes: That would be all. Thank you for your listening.