## Slide 1
Active RIS vs. Passive RIS: Which Will Prevail in 6G?
Linglong Dai
17th May, 2022
Department of Electronic Engineering
Tsinghua University

## Slide 2
Existing passive RIS
Proposed active RIS
Conclusions
Basics of RIS
Outline

## Slide 3: What is Reconfigurable Intelligent Surface (RIS)?
  A surface of reconfigurable metamaterials
  Control the propagation of electromagnetic wave
  Manipulate the channel to improve the signal quality
Traditional wireless communications:
Heavily rely on the environment
RIS-aided wireless communications:
Control the environment
E. Basar, M. Di Renzo, J. De Rosny, M. Debbah, M. Alouini, and R. Zhang, “Wireless communications through reconfigurable intelligent
surfaces,” IEEE Access, vol. 7, pp. 116753-116773, Jul. 2019.
RIS
Promising technology for future 6G communications

## Slide 4
Existing passive RIS
Proposed active RIS
Conclusions
Basics of RIS
Outline

## Slide 5
RIS consisting of a large number of passive elements
Negligible thermal noise, low cost, low power consumption
Realization of the existing passive RIS
Passive RIS
input
output
patch
phase- shift
circuit
Passive element
L. Dai, B. Wang, M. Wang, X. Yang, J. Tan, S. Bi, S. Xu, F. Yang, Z. Chen, M. D. Renzo, C.-B. Chae, and L. Hanzo, “Reconfigurable intelligent surface-based wireless communication: Antenna design, prototyping and experimental results,” IEEE Access, vol. 8, pp. 45913-45923, Mar. 2020. (IEEE Access Best Multimedia Award 2020)
RIS-aided commutations@2.3 GHz
RIS-aided commutations@28 GHz

## Slide 6
An example: passive beamforming for capacity improvement
Applications of the existing passive RIS
Transmitter
Transmitter
User
RIS
User
User
User
RIS
RIS

## Slide 7
The RIS-aided reflection link suffers large-scale fading twice
Fundamental limit: “Multiplicative fading” effect
W. Tang, M. Chen, X. Chen, J. Dai, Y. Han, M. Di Renzo, Y. Zeng, S. Jin, Q. Cheng, and T. J. Cui, “Wireless communications with reconfigurable intelligent surface: Path loss modeling and experimental measurement,” IEEE Trans. Wireless Commun., vol. 20, no. 1, pp. 421-439, Jan. 2021.
Passive RIS
BS
User
Passive RIS
User
(a) Atypical scenario
(b) Typical scenario
Signal model：
Product instead of summation
BS

## Slide 8
  BS (equipped with 4 antennas, transmit power 10 mW)
  RIS (equipped with 256 elements)
  4 User (equipped with 1 antennas)
Example
(0 m, 0 m)
(0 m, -40 m)
(200 m, 30 m)
x
BS
Passive RIS
(0 m, 0 m)
(500 m, 0 m)
y
user 1
user 2
user 3
user 4
System parameters

## Slide 9
Passive RIS can only achieve negligible capacity gain in typical communication scenarios
Example
Z. Zhang, L. Dai, X. Chen, C. Liu, F. Yang, R. Schober, and H. V. Poor, “Active RIS vs. passive RIS: Which will prevail in 6G? ,” arXiv preprint arXiv:2103.15154, Mar. 2021.
(a) Atypical scenario
(b) Typical scenario
Obvious 65%
capacity gain
Negligible 3%
capacity gain
How to overcome the “multiplicative fading” effect

## Slide 10
Existing passive RIS
Proposed active RIS
Conclusions
Basics of RIS
Outline
Notes: First, Let’s learn something about RIS.

## Slide 11
Concept of active RIS
Passive RIS: Reflect signals directionally without amplification
Active RIS: Amplify the reflected signals using power amplifiers
Active RIS
Transmitter
Receiver
incident
signal
reflected signal
with amplification
input
output
Passive RIS
input
output
patch
phase- shift
circuit
Receiver
incident
signal
reflected signal without amplification
Transmitter
power
supply
patch
phase- shift
circuit
reflection-type
amplifier

## Slide 12
Realization of active RIS
Feasible realizations of active reflection-type power amplifier
[1] J. Bousquet, S. Magierowski and G. G. Messier, “A 4-GHz active scatterer in 130-nm CMOS for phase sweep amplify-and-forward,”
IEEE Trans. Circuits Sys. I, vol. 59, no. 3, pp. 529-540, Mar. 2012.
[2] J. Kimionis, A. Georgiadis, A. Collado and M. M. Tentzeris, “Enhancement of RF tag backscatter efficiency with low-power reflection
amplifiers,” IEEE Trans. Micro. Theory Tech., vol. 62, no. 12, pp. 3562-3571, Dec. 2014.
[3] F. Farzami, S. Khaledian, B. Smida and D. Erricolo, “Reconfigurable dual-band bidirectional reflection amplifier with applications in Van
Atta array,” IEEE Trans. Micro. Theory Tech., vol. 65, no. 11, pp. 4198-4207, Nov. 2017.
[4] P. Keshavarzian, M. Okoniewski and J. Nielsen, “Active phase-conjugating Rotman lens with reflection amplifiers for backscattering
enhancement,” IEEE Trans. Micro. Theory Tech., vol. 68, no. 1, pp. 405-413, Jan. 2020.
[1]
[3]
[4]
[2]

## Slide 13
Signal model of active RIS
Different signal models of passive RIS and active RIS
(a) Passive RIS
(b) Active RIS
user
Amplification matrix
Additional noise introduced
by active components
patch
phase- shift
circuit
Phase shift matrix
phase- shift
circuit
reflection-type
amplifier
patch
BS
user
BS

## Slide 14
Validation of active RIS signal model
Experimental measurements of a fabricated active RIS element
incident
signals
reflected
signals
power
supply
patch
A fabricated active RIS element
Device Under Test
active RIS element
DC source
power supply
circulator
vector network
analyzer
spectrum analyzer
LNA
vector network analyzer
DC source
active RIS
element
circulator
pump
source
noise source

## Slide 15
Validation results
Measurement results
25 dB reflection gain
Thermal noise
is also amplified
(a) Reflection gain vs. frequency
(b) Noise power vs. reflection gain
Verify the correctness of the proposed signal model
Z. Zhang, L. Dai, X. Chen, C. Liu, F. Yang, R. Schober, and H. V. Poor, “Active RIS vs. passive RIS: Which will prevail in 6G? ,” arXiv preprint arXiv:2103.15154, Mar. 2021.

## Slide 16
Capacity maximization of active RIS aided MIMO
Three variables: BS precoding vector , phase shift matrix , and amplification matrix of active RIS
maximize
subject to
SINR of user k
BS power constraint
RIS power constraint
,
,

## Slide 17
Proposed joint precoding algorithm
Optimizing , , and alternatively
Lagrangian dual reformulation
Iteration
Derivation
Fractional programming
Fractional programming
optimize
optimize
optimize
optimize
,
,
,
,

## Slide 18
  BS (equipped with 4 antennas, transmit power 10 mW)
  Active RIS (equipped with 256 elements, reflect power 10 mW)
  4 User (equipped with 1 antennas)
Simulation for joint precoding design
(0 m, 0 m)
(0 m, -40 m)
(200 m, 30 m)
x
BS
Active RIS
(0 m, 0 m)
(500 m, 0 m)
y
user 1
user 2
user 3
user 4
Simulation parameters

## Slide 19
Active RIS can achieve noticeable capacity gain in typical communication scenarios
Simulation results
(a) Atypical scenario
(b) Typical scenario
1325%
129%
Active RIS can overcome the “multiplicative fading” effect
Z. Zhang, L. Dai, X. Chen, C. Liu, F. Yang, R. Schober, and H. V. Poor, “Active RIS vs. passive RIS: Which will prevail in 6G? ,” arXiv preprint arXiv:2103.15154, Mar. 2021.

## Slide 20
Experimental measurements of active RIS
Experimental measurements based on a 8×8 active RIS
Parameter | Setting
Frequency | 3.55 GHz
Bandwidth | 40 MHz
Polarization | Vertical (BS) Horizontal (user)
BS-RIS distance | 2 m
RIS-user distance | 3.5 m
AoA | 0°
Active RIS
BS
user
Device | Reflection AoD | Received Power | Data Rate
Metal plate | 15° | -110 dBm | 1.2 MHz
Active RIS |  | -100 dBm | 28.5 MHz
Metal plate | 45° | -105 dBm | 1.5 MHz
Active RIS |  | -95 dBm | 30 MHz
8×8 active RIS

## Slide 21
[1] E. Basar and H. V. Poor, “Present and future of reconfigurable intelligent surface-empowered communications,” IEEE Signal Process. Mag.,
vol. 38, no. 6, pp. 146-152, Nov. 2021.
[2] Z. Yigit, E. Basar, M. Wen, and I. Altunbas, “Hybrid Reflection Modulation,” arXiv preprint arXiv:2111.08355, Nov. 2021.
[3] R. Long, Y.-C. Liang, Y. Pei, and E. G. Larsson, “Active reconfigurable intelligent surface aided wireless communications,” IEEE Trans.
Wireless Commun., vol. 20, no. 8, pp. 4962–4975, Aug. 2021.
Future opportunities of active RIS
Other performance metrics optimization for active RIS
Channel estimation for active RIS aided system
Hybrid passive and active RIS architecture
Active RIS for other techniques, e.g., security, NOMA, MEC, etc.

## Slide 22
Existing passive RIS
Proposed active RIS
Conclusions
Basics of RIS
Outline

## Slide 23
  Basics of RIS
    Reconfigure the wireless environment
  Existing passive RIS
    Passively reflect signals without amplification
    Fundamental limit: “multiplicative fading” effect
    Only achieves negligible capacity gain in typical scenarios
  Proposed active RIS
    Reflect signals with amplification to overcome “multiplicative fading” effect
    New signal model verified by experimental measurements
    Achieves noticeable capacity gain in typical scenarios
    Recent test results based on an 8*8 active RIS
Conclusions
Passive RIS Active RIS

## Slide 24
Reproducible Research: http://oa.ee.tsinghua.edu.cn/dailinglong/
Thanks
Fan Yang
Zijian Zhang
Robert Schober
Vincent Poor